## Slide 1
Eco-Loop Building Agents
Autonomous Smart Building Control with Digital Twin & LLM Planning
• Problem Statement ID: 1
• Problem Statement Title: AI-Powered Autonomous Smart Building Optimization Challenge
• Theme: Smart Automation / Energy Efficiency
• PS Category: Software
• Student Name: Sagar Raj
• Student ID: 20524983

## Slide 2
PROPOSED SOLUTION
DETAILED EXPLANATION OF PROPOSED SOLUTION
▪ Autonomous Control Loop: Continually monitors building telemetry (indoor temperature, occupancy, weather, carbon intensity) and executes real-time control actions.
▪ AI Planning Agent: An LLM strategic planner dynamically calculates Energy Conservation Measures (ECMs) and updates temperature setpoints without human code changes.
▪ Digital Twin Sandbox: Simulates candidate control strategies over a 2-hour lookahead window before actuation to pick the most efficient strategy.
ADDRESSING THE CORE PROBLEM
▪ Replaces rigid rule-based schedules with demand-responsive, real-time thermodynamic planning.
▪ Reduces HVAC grid electrical loads during peak hours and high carbon intensity periods.
▪ Balances carbon reduction goals with occupant thermal comfort indices (PMV).
INNOVATION & UNIQUENESS
▪ Dual-model pipeline: Combines open-source LLM reasoning with a high-fidelity thermodynamic model.
▪ Zero-Trust Safety HUD: Deterministically validates AI output, falling back to RBC (Rule-Based Control) immediately if bounds are violated.
▪ Standardized MCP Server Integration: Uses Model Context Protocol tools to parse errors, read files, and handle simulation state-space telemetry.

## Slide 3
TECHNICAL APPROACH
TECHNOLOGIES & STACK
• Simulation Runtime: EnergyPlus (via eppy / PyEnergyPlus API integrations)
• Strategic Agent Brain: Open-Source LLMs (Qwen/Llama) with MCP Server tool-calling
• State Estimator / Twin: Lumped-Capacitance State-Space RC Thermodynamic Physics Model
• REST Services / API: FastAPI (Python-based ASGI web framework)
• Operations Interface: React + Vite (JavaScript runtime), Recharts, Tailwind CSS
CONTROL LOOP METHODOLOGY
1. Telemetry Capture: Sensors stream indoor temperature, weather forecasts, and grid emissions to the MCP server.
2. LLM Strategic Evaluation: The planner agent receives states and generates candidate HVAC control setpoints.
3. Digital Twin Sandbox Test: Simulates proposed setpoints 2 hours ahead to rank candidate strategies.
4. Safety Gate Check: Validates actuator boundaries, deadbands (>=1°C), and ramp-rates (<=3°C/step).
5. Execution / Fallback: Successful setpoints write to the EnergyPlus IDF file. Failures activate Rule-Based Control fallback.

## Slide 4
FEASIBILITY & VIABILITY
FEASIBILITY ANALYSIS
▪ Low Computational Footprint: The state-space RC model uses simple matrix mathematics, ensuring real-time simulation speeds.
▪ Standard compliance: EnergyPlus is the gold standard for building simulation. Integrating it via eppy guarantees industrial applicability.
▪ Robust Interface: Standard REST routes and JSON messaging ensure loose coupling between backend control and frontend visualizers.
POTENTIAL CHALLENGES & RISKS
▪ Model Latency: Prompt evaluation latency on high-parameter LLMs can lag. Capping loops under 2.5s is essential.
▪ LLM Hallucinations: Proposing out-of-bound temperatures that risk equipment damage.
▪ Data Sparsity: Missing weather or occupancy inputs during real-time sensor drops.
OVERCOMING STRATEGIES
▪ Caching & Asynchrony: Standard night-time setpoints leverage database caching. Parallel sandbox evaluations prevent latency pileup.
▪ Deterministic Safety Gate: Rejects unsafe commands at the system boundary—routing controls immediately to safe rule-based backups.
▪ Robust Fallback Routines: System fails safe automatically using baseline controllers if sensor connectivity is lost.

## Slide 5
PROJECT ARTIFACTS & RESULTS
IMPLEMENTATION PIPELINES
• Thermodynamic Digital Twin Model: Lumped thermal capacity models run inside the digital twin simulator, mapping temperature shifts step-by-step.
• Validation Gate Checks: Python validation libraries intercept commands, analyzing maximum setpoint slew-rates and cooling/heating deadbands.
• FastAPI REST Endpoints: Dashboard routes stream building status telemetry and receive controller weights live from UI adjustments.
QUANTITATIVE PERFORMANCE SAVINGS
17.3% HVAC Energy Savings: Reduces overall electricity consumed during a hot summer peak day compared to Rule-Based baselines.
17.8% Carbon Footprint Reduction: Shifts HVAC loads dynamically during clean grid hours, avoiding carbon intensity peaks.
30.5% Thermal Comfort Improvement: Stabilizes zone temperatures and minimizes comfort envelope deviations during occupancy spikes.
Zero Safety Incidents: Safety Gate successfully blocked 100% of injected actuator faults, maintaining fallback operations.

## Slide 6
RESEARCH & REFERENCES
ENERGYPLUS ENGINE CORE REFERENCES
• U.S. Department of Energy (DOE). EnergyPlus Energy Simulation Software. Developer manuals and input data schema structures.
• EPPy (EnergyPlus scripting in Python): A scriptable editor mapping IDF structures into editable python class objects.
MODEL CONTEXT PROTOCOL (MCP)
• Anthropic MCP Standard Specification: Standardizing communication between LLM agent nodes and sandbox operational tool APIs.
• Local server orchestration standards: Building decoupled agent modules that scale across multiple physical building modules.
ASHRAE STANDARDS & BUILDINGS SCIENCE
• ASHRAE Standard 55: Thermal Environmental Conditions for Human Occupancy. Evaluates Predicted Mean Vote (PMV) boundaries.
• Lumped Parameter building modeling structures: State-space RC network designs for fast digital-twin approximations.